## Slide 1
Towards “optimal”
GEM zigzag
readout plane layout
part#1
Alexander Kiselev
EIC R&D Tracking Meeting
Oct,05 2015

## Slide 2: This talk
Known issues with the present zigzag geometry (briefly)
Layout of (potentially) better strip configuration
“Naïve” simulation results for 1D strips
Other ideas (multi-strip charge sharing, TPC pads, etc)
Future plans

## Slide 3: More broad context
part#1: motivation; ideas; goals; linear strip case (ideal model)
part#2: RICH GEM readout plane layout optimization
part#3: linear strip case (ANSYS modeling)
-> today!

## Slide 4: Motivation(s) for this study
Complications with FNAL test run data analysis persistent over several months
Discussions at Temple University in May
Summary first shared by Bob in August (see presentation from Sep,14 2015)
Other “background” thoughts: ILD-style TPC needs; RICH readout pad issues
Strongly non-linear behavior of residuals after weighted mean centroid calculation
DNL correction depends on the electron cloud charge footprint size
Wide “flat” regions around strip centers (where charge is collected by a single strip)
-> the same origin: suboptimal charge sharing between neighboring strips
Can we do better?

## Slide 5: The ultimate goals of this exercise
Design - first on paper - strip layout which (ideally):
Does not show (almost) any DNL in weighted mean centroid calculation
Has weighted mean centroid unbiased for a wide range of charge cloud footprint sizes
Avoids “flat” regions (so always yields sufficient charge sharing between strips)
Simulate ideal layout performance for typical strip (pad) application cases
Eventually: model appropriate physical layout in ANSYS

## Slide 6: Simulation environment
Use custom ROOT scripts (~2000 lines; can be shared upon request)
No “physics” involved (see other assumptions below)
Consider to cover ~100% of the readout plane by electrodes -> no electric field distortions -> therefore “what you see is what you get” for electron-to-strip correspondence during charge collection phase;
Ignore bottom GEM foil holes either
Work mostly with gaussian distributions (cloud shape, pedestal noise, etc)
Typically assume no cross-talk
-> NB: eventually will have to introduce strip-to-strip gaps and use ANSYS

## Slide 7: Simulation & analysis configuration
Default (basic) parameters:
104 e- signal level (CPU-driven; sufficient to avoid cloud shape fluctuation effects)
2% pedestal-noise-sigma-to-signal ratio; gaussian pedestal noise with a mean of 0
2 mm pitch in X-direction (across the strips)
400 mm electron cloud footprint size (BNL micro-drift GEMs); gaussian shape; width will be varied for X- & Y-directions separately, since they underline different effects
500 mm Y-period of strip geometry (not a dominant effect for above parameter set)
Typically calculate plain weighted mean across 3 strips; no thresholds
-> these parameters conveniently bring us to ~60 mm spatial resolution level

## Slide 8
Present design model

## Slide 9: BNL & FIT configurations
Try to construct “equivalent” configurations with 100% of readout plane covered by electrodes (easy to model charge collection without any sophisticated software); do not pretend for a good description, just want to see qualitative picture
So make an assumption, that electric field distortions (compared to uniform field) are such, that gaps are “shared” 50:50 between neighboring strips
-> then BNL design strips “under-bite” each other in terms of tip-to-neighbor-strip-center distance by ~200 microns; and FIT is in fact even worse (~450 microns)!

## Slide 10: FIT-like zigzag model
“No charge sharing” zones roughly half X-pitch wide are seen in the model plot
real-life picture (6.0 x 8.0 mm2 area)
~equivalent model with 100% coverage
-> left picture: here and on all similar plots later the area of 10x10 mm2 is displayed (so 5 strips wide); strips oriented vertically (centers shown); watch X-pitch and Y-period as indicated;
In other words: neighboring strip overlap region is only ~1.1 mm out of 2.0 mm strip-to-strip range in FIT case

## Slide 11: Disclaimer
This simplistic 100% occupancy model may or may not reflect essential FIT design performance features (which may also depend on hardware specifics, analysis strategy, etc)
Therefore by no means conclusions must be directly applied to the FIT design case
Yet some hints can be taken of course
-> change “under-bite” value from 450 mm to 500 mm (for illustrative purposes)
and remove FIT label; 500 mm roughly means, that neighboring strips overlap
in X-direction only in the 1 mm wide area for the 2 mm X-pitch case (and in fact
linear charge sharing model is established in this area);

## Slide 12: “50%-overlap” zigzag: charge sharing
charge sharing (point-like e- cloud)
-> right picture: here and on all similar plots later the horizontal area of 4mm (so covering 2 strips) is displayed (see magenta rectangle in the left plot); strip centers are at 0mm, 2mm and 4mm; either point-like electron source or gaussian shape cloud (watch plot description);
strip layout
“No charge sharing” zone ~1mm wide is seen

## Slide 13: “50%-overlap” zigzag: charge sharing
charge sharing (400 mm wide e- cloud)
Charge sharing becomes better with smeared e- cloud; yet suboptimal
strip layout
-> left picture: here and on all similar plots later electron cloud size (1- & 2-sigma contours) shown when relevant; NB: X- and Y-width can be different for procedural / illustrative purposes!

## Slide 14: “50%-overlap” zigzag: weighted mean
-> top picture: here and on all similar 2D plots later the horizontal area of 4mm (so covering 2 strips) is displayed (see dashed magenta rectangle in the strip layout plot); strip centers are at 4mm, 6mm and 8mm; residual axes range: 1mm; right panel: residuals vs X-coordinate (across strip direction); left panel: 1D projection; no DNL correction; clusters forced to be 3-strip-wide;
3-strip clusters; no threshold applied
Differential non-linearity is clearly seen

## Slide 15: “50%-overlap” zigzag: weighted mean
Same as last slide, but 200 micron wide cloud
Cluster width dependence is clearly seen
Linear region in 2D plot around 6mm (strip center) is caused by “no charge sharing” situation and can not be recovered
Linear regions in 2D plot around 5mm and 7mm (in between strips) are caused by wrong default coefficients in weighted mean formula (NB: only ~half of the 2mm “cell width” is actually position-sensitive in this design!)

## Slide 16: “50%-overlap” zigzag: weighted mean
Same as last slide, but 600 micron wide cloud
Cluster width dependence is again seen
This dependence is different for 200, 400 and 600 micron cases -> can not be properly corrected for unless cloud width is known and/or more or less fixed

## Slide 17: “50%-overlap” zigzag: weighted mean
Consider extreme 200 micron cloud case
Infamous “flat” regions in reconstructed X-coordinate are present; detector has no positional sensitivity there
NB: a scaling factor of 2 is applied to the weighted mean calculation in ~1mm wide “sensitive” region in order to obtain correct reconstructed coordinate
-> a $100 question: which spatial resolution to quote?
NB: 2D plot here has a different meaning here!

## Slide 18
Linear response model

## Slide 19: Zoom into FIT zigzag layout
In fact all we need is to properly arrange charge sharing as f(X) in the indicated rectangular area; the rest is driven by translational symmetry in X- and Y-directions
And it can be, that zigzag is visually simply not the best representation of the otherwise obvious approach how to attain this

## Slide 20: Linear response “fish spine”
charge sharing (400 mm wide e- cloud)
strip layout
Much better charge sharing (a single strip never collects >85% of the signal)
And - more important - it exhibits response linearity in X-direction (see next slide)

## Slide 21
If electron cloud looked like this, it would be obvious, that as long as it moves from left to right side of the 2mm long rectangle, green strip collected charge will linearly go down from 1 to 0 and yellow strip charge will linearly go up from 0 to 1
Linear response “fish spine”

## Slide 22
It turns out, that this property also holds for “normal” (wide) electron clouds
More than that, gaussian distribution shape is not required; cloud should just be left-right symmetric and the distribution width should only be “sane” compared to the pitch in X-direction (will consider [200 .. 800] mm range)
X-pitch is just a trade-off between channel count and spatial resolution
The only required property of Y-direction is to establish periodic structure with a period comparable or smaller than the electron cloud sigma (to wash out response “beating” as a function of Y-coordinate)
Linear response “fish spine”

## Slide 23: “Fish spine”: nothing new?
“diamond band”
“fish spine”
Right plot layout: start with the left plot pattern and flip right half of every triangle
NB: both patterns are equivalent in charge sharing properties

## Slide 24: “Fish spine”: nothing new?
“diamond band”
Right plot layout: flip every second in vertical direction parallelogram in the left plot and squeeze Y-direction by a factor of 2
Charge sharing properties do not change; zigzag has better connectivity and is perhaps more suited for 1D applications; “diamond band” is more versatile (see later)
our old well-known zigzag 

## Slide 25: “Fish spine”: nothing new?
So (as usual) everything good is already invented since years 
Well, almost everything, keep reading …
“linear response zigzag”
LEGS TPC readout plane
Don’t they look similar ?!
-> will exclusively use “diamond band” configuration in the following (as sort of more “generic” one)

## Slide 26: “Diamond band”: weighted mean
First “extreme” case (200 mm cloud): looks great!, no artifacts
Plain weighted-mean centroid over 3 strips (max channel + two neighbors) with no threshold cut yields ~60 mm spatial resolution across the entire 2mm wide “cell”

## Slide 27: “Diamond band”: weighted mean
Second “extreme” case (600 mm cloud): looks the same
-> no DNL correction & no cluster width selection needed to get to ~basic performance level: turnkey detector for data analysis

## Slide 28: “Diamond band”: weighted mean
Rectangular cloud distribution in X (sigma matching 400 mm gaussian): looks the same
-> no cloud shape dependence (as long as it is left-right symmetric and not “too wide” compared to X-pitch)

## Slide 29: “Diamond band”: weighted mean
400 mm cloud and 1-sigma threshold cut
-> can clearly improve the resolution a bit further, but at a cost of (small) DNL and other (small) artifacts

## Slide 30: “Diamond band”: spatial resolution
~Constant in a relatively wide dynamic range of width values (~4x); must be good enough even for a typical TPC application
… as a function of e- cloud width
… as a function of pedestal noise
-> analysis artifact: should consider >3 strip wide clusters
Linear dependence on the noise variance, so: signal-to-noise ratio is essential (as expected)
-> default configuration

## Slide 31: “Diamond band”: spatial resolution
… as a function of X-pitch
… as a function of Y-period
Linear dependence on the X-pitch
The effect is understandable: spatial resolution is driven by charge sharing derivative over X as a function of X; smear it over wider region – spoil resolution
Yet there is no apparent negative effect up to a ~1mm period or so (see 2D layout requirements later)
-> charge spread becomes insufficient to wash out periodic structure effects in Y-direction

## Slide 32: Back to the $100 question
So for the 50%-overlap zigzag model we simulated ~30 mm spatial resolution in the 1mm wide “overlap” region and no sensitivity (thus ~300 mm RMS of the uniform distribution) for the other half of 2mm wide X-cells
Possible answers:
Detector has indeed 30 mm resolution, but is only 50% efficient (discard “flat” regions)
Detector has 30 mm resolution on 50% of tracks and ~300 mm on the other 50%
Detector has an average resolution which is equal to RMS of 30 mm wide gaussian on top of 1mm wide uniform distribution taken in proportion 50:50
If the readout plane gets changed to a 100%-overlap zigzag (or “diamond band”) configuration with the same X-pitch & Y-period (and pedestal noise as well as the signal level are also kept the same), resolution will become 2x 30 mm (and this factor of 2x is essential here!); to gain it back (in the scope of the considered model) one needs to improve signal/noise ratio by the same factor of 2x; NB: once again, it’s a model – we basically assume, that signal/noise ratio has a dominant effect on the spatial resolution
-> which resolution to quote ?!

## Slide 33: “Diamond band”: spatial resolution
Almost constant across the strip width
Some variation seen, presumably due to 1) binomial error expression “artifact” (similar to calculated efficiency stat.error behavior at values ~100% vs ~50%), 2) naïve 3-strip cluster selection is suboptimal for hits in the ~middle between strips
… as a function of X-coordinate
… as a function of signal amplitude
-> charge cloud center determination becomes poor at low electron count; NB: remember, naïve gaussian cloud shape model was considered so far

## Slide 34
Other configurations

## Slide 35: ILD-style TPC readout pads
If works for long strips, should be good for short pads as well (2x6 mm2 here)
Y-overlap configuration allows to improve Y-resolution by a factor of 2
Same configuration can clearly be implemented for endcap (radial) geometry
conventional zigzag
the same, but with with Y-overlaps

## Slide 36: Push charge sharing even further?
-> NB: can not do this in “fish spine” model; but “diamond band” also works …
“500mm-stretched zigzag” layout
charge sharing (400 mm wide e- cloud)
Spread charge cloud over ~3 strips in order to 1) determine its width on “per track” basis, 2) possibly flatten spatial resolution profile over the whole X-range;

## Slide 37: Is some 2D configuration possible?
“diamond band”
the same, with every 2-d band removed
“Spare” space can be used for conventional straight strips; this gives Y-plane with a pitch of 2x the Y-period of the original “diamond band” pattern; remaining “diamond band” elements should be inter-connected using vias on a double-sided kapton or a 2-layer PCB
-> so the answer is YES!

## Slide 38: Is 2D “diamond band” possible?
conventional “diamond band”
the same, with elements rotated by 45 degrees
Charge sharing scheme and spatial resolution are the same for both patterns
One can again consider to remove every 2-d band …

## Slide 39: Is 2D “diamond band” possible?
“diamond band”, even rows (X)
… and replace odd rows by “diamond bands” with elements, aligned along X direction
NB: modeled spatial resolution of these new X- and Y-planes will be a factor of 2 worse, than the original “complete” configuration (signal-to-noise ratio goes down!)
“diamond band”, odd rows (Y)

## Slide 40: Is 2D “diamond band” possible?
2D “diamond band”
X&Y-rows are (almost) identical geometrically and exhibit linear “diamond band” properties as long as Y-pitch can be maintained small enough
Conventional connection scheme requires 1 via per every small diamond and a 3-layer PCB
Another option: use double-sided kapton and put 2 vias per every small diamond; they get inter-connected in a chain via short bridges on the back side the same way as previously suggested 3D COMPASS-style GEM readout (drawback: one via bad – the hole strip gone); NB: bridges should be oriented at 90 degrees to the upper side bands and also physically allocated in bands -> so no conflict between X&Y-rows in strip layout is anticipated
-> sort of tricky, but in general the answer is also YES!
Even rows measure X coordinate; odd rows measure Y coordinate; both on the “upper” surface

## Slide 41: Other “diamond band” configurations
Just in case this was not enough , consider the following: 45-degree bands are pretty much independent from each other, therefore:
They can be made of different width (so XY-planes will see different charge fraction)
Their “diamonds” can be of different length (so XY-planes will have different pitch)
“Diamonds” can be staggered from row to row differently (see XY-configuration as an example), yielding plane orientation at any sane angle with respect to the band direction
One can therefore (as long as Y-pitch can be made small enough for the particular e- cloud width configuration) add to the XY-set a 3-d plane say at 45 degrees, with somewhat poor resolution (use smaller band width and longer diamonds -> large pitch) with the only purpose to help resolving multiple hit events; “diamond” inter-connection can still be done using vias with a double-sided kapton (no problem to arrange 3 groups of parallel bridge bands on the back side) or a 4-layer PCB
Was mentioned already, yet: “diamond bands” do not need to be straight; in particular endcap configuration suggests circular ones to arrange 1D planes
-> NB: regular strips are also fine (they would go at 45 degrees to XY planes as well)

## Slide 42
Real life & outlook

## Slide 43: Real life complications
Gaps are necessary between strips
will distort the electric field and affect linearity properties
ANSYS modeling should help to (partly) recover this
Pad size limitations exist; especially for configurations with vias
Cross-talk influence
Effects of increased strip-to-strip capacitance
Gain variation across the strips
Non-gaussian e- cloud shape (effect of GEM holes, etc)
Other suggestions?

## Slide 44: “Diamond band”: cross-talk
400 mm cloud; constant cross-talk at 5% level
-> clearly an issue if not unfolded!
-> cross-talk in this simplistic model is a single-parameter linear transformation, which can be inverted and easily applied to “raw” amplitudes

## Slide 45: “Diamond band”: cross-talk
constant cross-talk at 40% level, unfolded
-> constant (and known) cross-talk is not a problem even at pretty high level
-> even if unknown, it is a single parameter, which can be tuned easily (just make 2D plot flat again); nothing to compare in complexity to full DNL correction

## Slide 46: “Diamond band”: cross-talk
fluctuating cross-talk at 0% level and 5% variance
-> yes, then it becomes an issue
-> worst case is left-right asymmetric cross-talk with either unknown level or non-zero variance

## Slide 47: Outlook
Last week we (Craig, Bob & AK) talked to Graham Smith and Bo Yu from BNL instrumentation; expert opinion:
Interesting; not really something new (except for 2D) or exciting, but interesting
Have to consider finite feature size of the plotter (25 mm or so)
Tips should better not be more narrow, than 100 mm
Strip-to-strip gaps no way more narrow, than 50 mm and this is already pushing
In case of PCBs: via diameter of 150 mm must be observed (Bob measured vias on a double-sided kapton – see the picture – and it looks like there ~70 mm possible)
Will work with ANSYS package (or perhaps deal with Laplace equation by hand) in order to design the strip shape which exhibits linear charge sharing scheme after strip-to-strip gaps are introduced and other limitations applied
Next week meeting: RICH GEM pad plane design with charge sharing
-> at this point perhaps Tech Etch should be involved